## Slide 1: Lab 3
FPGAs as Accelerators
Embedded Systems ECE340
Ioannis Athanasiadis-03491
Stavros Stathoudakis-03512

## Slide 2: Introduction
Goal: Implementation of LSAL Algorithm as FPGA Accelerator
Tools:
  Valgrind (Code Profiling)
  Intel Advisor (Code Profiling)
  Vitis HLS
  Visual Studio Code
  ✨FanTAsY ✨

## Slide 3: A Few Things About LSAL
Stands for Local Sequence Alignment Algorithm
Used in Bioinfomatics (More on that later)
Input:
  Database[M] string
  Query[N] string
Output:
  Direction Matrix [M*N]
  Similarity Matrix [M*N]
  Max Index

## Slide 4: Submitted Files
FPGA folder contains the source code files need to run the accelerator
Software folder contains the source code files of the optimized
  Makefile with options on cpu arch, debug flag and code profiling automation
The submitted files follow the following format.
├── FPGA
│ ├── lsal.cpp
│ └── lsal_host.cpp
├── Software
│ ├── lsal_optimized.cpp
│ └── Makefile
└── Report.pdf

## Slide 5: Software
Workflow
  Implementation
  Profiling
  Code Optimization
  Comparison
Debug flag
Prints the output of LSAL
Known Input -> Known Outputs
Profiling Flag
Executes valgrind’s callgrind tool
Auto-opens kcachegrind to visualize data

## Slide 6: Software Unoptimized
Calculation of Similarity and Direction Matrices Row-Wise
  Save the location of element with max similarity
Direction Priority: C, NW, N, W
Edge cases:
  First row and first column (N & NW, W & NW)
  Loop Unrolling

## Slide 7: Software Unoptimized
The results for a varying number of array sizes
x86 78.82% faster than ARM
x86 vs ARM Unoptimized (sec) |  |  |  | 
Ν | Μ | ARM | x86 | Difference
32 | 32 | 0.000098 | 0.00002 | 79.5918%
32 | 65536 | 0.175177 | 0.037108 | 78.8169%
256 | 65536 | 1.402216 | 0.303335 | 78.3675%
256 | 300000 | 6.417753 | 1.388256 | 78.3685%

## Slide 8: Software Optimized
Branching
  Uncertainty is a slow nightmare
  Reduce commands for branching (if, for etc)
  Unrolling as weapon
  Used extensively for the edge cases
Division & Modulo
  Hard to process
  Eliminate where possible
  Nested for-loops
    Eliminate index % N, index / N
Defines
  Use #define instead of constant variables

## Slide 9: Software Optimized
x86 vs ARM Optimized (sec) |  |  |  | 
Ν | Μ | ARM | X86 | Optimization
32 | 32 | 0.000045 | 0.000015 | 66.6667%
32 | 65536 | 0.076079 | 0.024057 | 68.3789%
256 | 65536 | 0.586488 | 0.196926 | 66.4228%
256 | 300000 | 2.685104 | 0.897239 | 66.5846%

## Slide 10: Software Optimized
Roofline Model
  Red Circle represents the unoptimized version
  Red square represents the optimized version
    Less dependent on memory bandwidth
    Better parallelism

## Slide 11: Software Optimized
x86 (sec) |  |  |  | 
Ν | Μ | Unoptimized | Optimised | Optimization
32 | 32 | 0.00002 | 0.000015 | 25.0000%
32 | 65536 | 0.037108 | 0.024057 | 35.1703%
256 | 65536 | 0.303335 | 0.196926 | 35.0797%
256 | 300000 | 1.388256 | 0.897239 | 35.3693%
ARM (sec) |  |  |  | 
Ν | Μ | Unoptimized | Optimised | Optimization
32 | 32 | 0.000098 | 0.000045 | 54.0816%
32 | 65536 | 0.175177 | 0.076079 | 56.5702%
256 | 65536 | 1.402216 | 0.586488 | 58.1742%
256 | 300000 | 6.417753 | 2.685104 | 58.1613%

## Slide 12: Hardware
Workflow
  Optimization
  C Simulation
  Synthesis Design Report
  QEMU Emulation
  Native test & Timing

## Slide 13: Hardware Optimizations
Algorithmic Optimizations
  Diagonal Parallelism
    2 Nested loops
      Outer: Diagonals
      Inner: Elements of diag.
  Data Dependencies
    Similarity Matrix doesn’t need to be outputted
    Only need 2 diag. above
    Double the size of current diagonal buffer to fight write-after-read during the ending-starting on iteration

## Slide 14: Hardware Optimizations
HLS Optimizations
  Array buffers
    Block RAM or Flip-Flops
    Cyclic, Block or Complete
    Partition or Reshape
  Arbitrary Elements
    Reduce the size of buses in use
    Save bandwidth
    Database, Query and direction matrix are 3-bit elements
    Other elements such as max_index shouldn’t be limited unless it is made sure they are kept in bounds

## Slide 15: Comparison
FPGA vs x86 |  |  | 
Ν | Μ | x86 | FPGA
32 | 32 | 0.00002 | 0.0008173
32 | 65536 | 0.037108 | 0.1757924
256 | 65536 | 0.303335 | 2.176